## Slide 1: ANALYSIS OF FIRE ONBOARD ROPAX FERRY: Overview to the investigation cases of fire onboard roro passenger ferry in Indonesia
Presented on:
24th Marine Accident Investigators International Forum Meeting
Antalya, Turkey
7-11 June 2015

## Slide 2: Ferry Fire Accidents
Philippine - Dona Paz (1987): 4 xxx fatalities
Baltic Sea - Scandinavian Star (1990): 150 fatalities
Philippine - SuperFerry 14 (2004): 60 fatalities
Italy Sea - Vincenzo Floria (2009)
Ionian Sea (off Italy Coast) – Norman Asturias (2014): 8 fatalities
Japan sea – Sunflower Daisetsu (2015): 1 fatality
Indonesia??

## Slide 3: Indonesian Domestic Ropax ferry

## Slide 4: Indonesian Ferry Service
2014 Data:
Fleet:
258 Ferry Ships (15 Pioneer ferry ships)
Lane:
48 Commercial, 169 subsidise
Loading Capacity:
50 Thousand Pax,
6 Thousand Vehicles
Ports:
210 Ferry Ports
2014 Data:
Productivity:
62. 036. 587 Pax
7. 713. 925 Vehicles

## Slide 5: CASES OF FIRE ONBOARD FERRY ROPAX IN INDONESIA (2006 – 2014)

## Slide 6: Reviewed Cases
No | Year | Cases | Fire origin (suspected) | Consequence/s | 
 |  |  |  | To Ship/Cargo | To Passengers
1 | 2006 | MV. Lampung | Main Engine Turbocharge (MS) | Disabled the ship due to heavy damage | Minor Injuries to crew and pax
2 | 2007 | MV. Nusa Bhakti | Non-marine use electric cable (MS) | Medium damage in engine room | No Fatality
3 |  | MV. Levina I | Cargo carried by a vehicle (CD) | Major Damaged to Construction and Acc | 50 fatalities, 18 Minor Injuries
4 | 2008 | MV. Dharma Kencana I | Rolled mooring line (AD) | Heavy Damage to Accommodation area | 1 Fatality
5 | 2009 | MV. Mandiri Nusantara | Cargo carried by a vehicle (CD) | Heavy damaged to the ship | 6 Fatalities
6 | 2011 | MV. Laut Teduh-1 | Vehicle onboard cardeck (CD) | Major Damage to the above water Constr. | 7 Fatalities
7 |  | MV. Salvia | Main Engine (MS) | Minor damaged | No Fatality
8 |  | MV. Musthika Kencana II | Vehicle onboard cardeck (CD) | Total Loss | No Fatality
9 |  | MV. Marina Nusantara | Vehicle onboard cardeck (CD) | Major Damage to the above water constr. | 6 Fatalities
10 | 2014 | MV. Gelis Rauh | Cargo carried by a vehicle (CD) | Disabled the ship due to heavy damage | No Fatality

## Slide 7
TYPICAL CONSEQUENCES BASED ON EACH TYPE OF FIRE ORIGIN:
Accommodation Space : Medium to Major Damage, Fatality/s
Car deck : Total Loss, Heavy Damaged, Fatalities
Machinery Space : Medium to Heavy Damaged

## Slide 8: RISK OF FIRE ON FERRY ROPAX: CARDECK
Condition of Vehicle
Cargo Handling
Layout and placement
Inspection of cargo

## Slide 9: HFACS Model (by Shappel and Wiegmann - 2000)

## Slide 10: CONTRIBUTORY FACTORS

## Slide 11: CONTRIBUTORY FACTOR ANALYSIS RESULTS ORGANISATIONAL INFLUENCE

## Slide 12: CONTRIBUTORY FACTOR ANALYSIS RESULTS SUPERVISION

## Slide 13: CONTRIBUTORY FACTOR ANALYSIS RESULTS PRE-CONDITION

## Slide 14: CONTRIBUTORY FACTOR ANALYSIS RESULTS UNSAFE ACT

## Slide 15: UNSAFE ACT – FIRE ONBOARD FERRY

## Slide 16: SEMOMAP’s Stages of Accident (Phase-1-3)

## Slide 17: Pattern of Failure in RORO Ferry Fire Accident

## Slide 18: ACCIDENT DEVELOPMENT STAGES

## Slide 19: General Issues in Fire onboard Ropax
Shortcoming of Equipment
Complacency
Crew Preparedness
  Training
  Familiarisation
Control of Passengers
Operational Issues
Unreported cargo inside Vehicles

## Slide 20: Conclusion
Fire onboard Ferry Ropax has significant degree of difficulties;
Control of passengers;
Awareness and readiness of the crew;
Consistent supervision to the ferry operation.

## Slide 21
Thank You
Jl. Medan Merdeka Timur No 5, Jakarta. 10110 INDONESIA
Telp. (+62) 21 384 7601; Fax (+62) 21 351 7606
Website :
http://www.dephub.go.id/knkt
E-mail :
knkt@dephub.go.id;
marine.knkt@dephub.go.id